## Slide 1: Activity Board

## Slide 2: Activity Board Übersicht
USB-C charging
Master Module
Battery Pack
Master Select
Sound System
Activity Bus (I2C BUS)
Music Gadget
Data Library microSD Card
USB-C upload
USB-C upload
Buttons Panel
Speaker
Volume Control
Indicators Panel
Music Controller
Music Gadget consists of 4 buttons and 4 LED indicators. Every button is accompanied by a picture and corresponds to an individualsound in the master sound library. If a button is pressed the corresponding sound is played and the LED indicator lights up.
Sun Gadget
Gadgets are activity modules with electronic or mechanical parts to play with. Gadgets will be placed independently on a wooden board with a central master module providing power supply and other common features. Gadgets range from simple mechanical knobs to electronic games with OLED display (e.g. tretris, snake, pong).
Time of Day Panel
Sunlight Panel
Sun Controller
Sun Gadget consists of a "Time of Day" knob to turn and control the "Sunlight". The knob is round and points to phases during a normal day (early morning, late morning, midday, afternoon, evening, night) identified by symbols. Turning this knob controls the brightness of the "Sunlight" represented by a round convex lid illuminated by a white LED. If exact positions are hit a song correspondingt to the phase is played (e.g. at "night" a lullaby).
Pong Gadget
OLED Display
Controller Panel
PingPong Controller
Pong Gadget is a simple implementation of the ping pong game. It consists of a small OLED display (1 or 2 inch) and a Controller Panel with "start / stop" buttons and a potentiometer to control the racket. It also plays "ping / pong" sounds when rackets hit the "ball".
Display System
TFT Display
Rotary Encoders

## Slide 3: Standard Specifications
JST 2.54 XH (2 poles)
JST 2.54 XH (4 poles)
USB (4 poles)
Soldered Connection
x
Resistor
x µF
Capacitor
USB Pin | Ardino Pin | Kabelfarbe | Bedeutung
G | GND | schwarz | Power minus
VBUS | 5V | rot | Power plus
D- | A4 | weiß | SDA
D+ | A5 | gelb | SCL

## Slide 4: Standard Layout Gadget
USB Pin Mapping
G : GND
D- : SDA (Ardino A4)
D+ : SCL (Ardino A5)
V : 5V
I2C Sockets Board
Gadget A Panel Port USB
Gadget B Panel Port USB
Gadget C Panel Port USB
Gadget D Panel Port USB
Arduino Nano
General Gadget Board
Service Panel Port (USB)
I2C Bus Panel Port (USB)
A5
A4
D+
D-
GND
V
5V
GND
other component
other component
other component
other component

## Slide 5: Activity Bus Board

## Slide 6: Activity Bus Board
Activity Bus Board
Peripherical 1 Panel Port USB
Peripherical n Panel Port USB
Gadget 1 Panel Port USB
Gadget 2 Panel Port USB
Power Panel Port USB
2P4T Drehregler
2 Pull-Up-Widerstände am Master Module
5 kΩ (normalerweise 2,2 - 4,7 kΩ)
von Master SDA nach VCC und
von Master SCL nach VCC
5k
5k
CD4066 Multiplexer
Masterselect
wird gesteuert von einem 2P4T Drehregler
der Drehregler versorgt die Gadgets mit VCC/GND : immer nur einen zu einer Zeit
der Masterselect öffnet und schließt die Kanäle am Multiplexer, wenn gedreht wird
«Arduino» Masterselect

## Slide 7: Connecting Periphericals and Gadgets via Activity Bus Board
Activity Bus Board
USB
USB
USB
USB
USB
Peripherical 1
USB
Peripherical …
USB
…
USB
Gadget 1
USB
Gadget …
USB
USB Pin Belegung
G : GND
D- : SDA (Ardino A4)
D+ : SCL (Ardino A5)
V : VCC (5V)

## Slide 8: CD4066 Specification

## Slide 9: CD4066 Gadget Dispatch Block
# | Gadget | Drehschalter | Activity Bus | Activity Bus | Drehschalter | Gadget | #
1 |  |  | SDA | 5V |  |  | 1
2 | SD1 |  |  | 10 kΩ gegen GND | GC1 |  | 2
3 | SC1 |  |  | 10 kΩ gegen GND | GC2 |  | 3
4 |  |  | SCL | SCL |  |  | 4
5 |  | GC1 | 10 kΩ gegen GND |  |  | SC2 | 5
6 |  | GC2 | 10 kΩ gegen GND |  |  | SD2 | 6
7 |  |  | GND | SDA |  |  | 7
1 |  |  | SDA | 5V |  |  | 1
2 | SD3 |  |  | 10 kΩ gegen GND | GC3 |  | 2
3 | SC3 |  |  | 10 kΩ gegen GND | GC4 |  | 3
4 |  |  | SCL | SCL |  |  | 4
5 |  | GC3 | 10 kΩ gegen GND |  |  | SC4 | 5
6 |  | GC4 | 10 kΩ gegen GND |  |  | SD4 | 6
7 |  |  | GND | SDA |  |  | 7

## Slide 10
5V
GND
Gadget 1
Gadget 2
SDA SCL
SDA SCL
GC1
GC2
V5
GND
Gadget 4
Gadget 3
SDA SCL
SDA SCL
GC3
GC4
V5
GND
SDA
SCL

## Slide 11: Power Supply Board

## Slide 12: Power Supply Board
TP4056 Charging
OUT+
OUT-
B+
B-
Battery Pack 3,7 V – 5200 mAh
Red (+)
Black (-)
Power Switch on / off
MT3608 Step Up
VIN-
VIN+
OUT+
OUT-
Charging Panel Port (USB)
220
Power LED
Power Supply Board
Power Output Panel Port (USB)
Charging
use any USB chager
Power Mapping
only V5 and GND are provided
USB Pin Belegung
G : GND
V : VCC (5V)

## Slide 13: Power Board Panel Laser Template Controls
Panel
inkl. nut : 90 x 94
innen : 80 x 84
Platine
Höhe : 30
Battery Pack
Höhe : 39
Controls Area
Höhe : 15
Breite : 80
Charging USB (links)
- Links :
USB
USB
SW

## Slide 14: Power Board Panel Laser Template Labels
Panel
inkl. nut : 90 x 94
innen : 80 x 84
Platine
Höhe : 30
Battery Pack
Höhe : 39
Controls Area
Höhe : 15
Breite : 80
Charging USB (links)
- Links :
USB
USB
SW
Fizz Bizz
Charge
Output
Master Switch
[Power Supply Module]

## Slide 15: Power Board Panel Laser Template Frame
Frame
außen : 115 x 120
innen : 79 x 84
Rand : 18
Fizz Bizz
power supply 5V=

## Slide 16: Sound Module

## Slide 17: Sound Module
Arduino Nano
Sound Module Board
5k
A5
A4
DFPlayer Mini
Pin 6
Pin 8
2
3
D11
D10
Player Pin Mapping
Pin 2 (RX) : D10 (TX) (1 k Ohm)
Pin 3 (TX) : D11
Pin 16 (busy) : D12
Sound Upload Panel Port (USB)
14
15
16
D12
D+
D-
GND
USB C Breakout Board
VBUS (left open)
Speaker Panel Port (Banana Sockets)
Red (+)
Black (-)
Volume Control
Rotary Encoder Mapping
CLK : D2
DT : D3
SW : D4
GND : GND
+ : 5V
1k
5V
Sound Upload Board Mapping
D+ : Pin 14
D- : Pin 15
GND : connected
VBUS : left open
1 7 (10)
5V GND
220
Player LED
GND
D9
D2 D3 D4
470 µF
Service Panel Port (USB)
Service Mapping
GND, D-, D+ pass thru
VBUS left open
connect computer for software upload and debugging
GND
5V
Sound Upload
connect computer USB
use explorer to manage sd card
Speaker
connect 8 Ohm 4 Watt
use banana connectors
5V and GND connections not shown in diagram
Activity Bus Panel Port (USB)
GND
5V
I2C Integration
Address: 0x10
Libraries:
  dfrobot/DFRobotDFPlayerMini
  paulstoffregen/Encoder
  arkhipenko/TaskScheduler

## Slide 18
DFRobotDFPlayerMini player;
SoftwareSerial playerSerial(11, 10); // RX, TX
… setup
playerSerial.begin(9600); player.begin(playerSerial, true, false);
loop player.next();
Arduino Pin auf Player Pin
D2 (TX) auf 10 (RX) braucht 1 k Ohm Widerstand
D3 (RX) auf 11 (TX)

## Slide 19: Numpad Module

## Slide 20: Numpad Module
Numpad Module Board
Activity Bus Panel Port (USB)
PCF8574
GND
VCC
Numpad
SCL
SDA
USB Pin Belegung
G : GND
D- : SDA
D+ : SCL
V : VCC (5V)
GND
VCC
PCF8574 | Numpad | Bedeutung
P0 | Pin 2 | row 1
P1 | Pin 7 | row 2
P2 | Pin 6 | row 3
P3 | Pin 4 | row 4
P4 | Pin 3 | col 1
P5 | Pin 1 | col 2
P6 | Pin 5 | col 3
P7 | unbelegt | col 4
https://github.com/RobTillaart/I2CKeyPad
I2C Integration
Address: 0x20
Library: I2CKeyPad

## Slide 21: Display Module

## Slide 22
Display Pin | ESP32 Pin | Description (at HSPI)
VCC | 3V3 | Power plus
GND | GND | Power minus
CS | GPIO 15 | SPI Chip Select
RST | GPIO 4 | Display Reset
DC | GPIO 2 | Data / Command
DIN (SDI, MOSI) | GPIO 13 | SPI-Datenausgang vom ESP32 (MasterOut-SlaveIn)
CLK | GPIO 16 | SPI Hardware-Taktleitung
BL | GPIO 17 (oder 3V3) | Hintergrundbeleuchtung regelbar (oder dauerhaft an)
Display Module Board
Activity Bus Panel Port (USB)
ESP32
TFT Display
GND
3V3
I2C Integration
Address: 0x11
Library: Adafruit
DIN
CLK
DC
RST
BL
13
16
2
4
17
CS
15
Service Panel Port (USB)
Service Mapping
GND, D-, D+ pass thru
VBUS left open
connect computer for software upload and debugging
Pegelwandler
USB Port | Pegelwandler | ESP32 | Description
VCC (5V) | HV | V5 | Power plus 5V
GND | GND | GND | Power minus
D- (SDA) | HV1 |  | SDA (high voltage)
D+ (SCL) | HV2 |  | SCL (high voltage)
 | LV | 3V3 | Power plus 3.3V
 | LV1 | GPIO 21 | SDA (low voltage)
 | LV2 | GPIO 22 | SCL (low voltage)
sd card module
sd card extender
SD-Modul | ESP32 Pin | Description (at VSPI)
3V3 | 3V3 | Power plus
GND | GND | Power minus
MISO | GPIO 19 | Master-In-Slave-Out
MOSI | GPIO 23 | Master-Out-Slave-In (parallel to DIN of Display)
CLK | GPIO 18 | Clock (parallel to CLK of TFT Display)
CS | GPIO 5 | Chip Select
HV
GND
LV
LV1
LV2
V5
GND
3V3
21
22
VCC --- HV GND --- GND D- --- HV1 D+ --- HV2
VCC
GND
MI
MO
CLK
V5
GND
19
23
18
CS
5
Rotary Encoder
14
27
32
33
26
25
SW
DT
CLK
DT
CLK
SW
Rotary | ESP32 Pin
CLK-LEFT | 32
DT-LEFT | 33
SW-LEFT | 25
CLK-RIGHT | 26
DT-RIGHT | 27
SW_RIGHT | 14

## Slide 23
# | Display | SD | PW | Rotary | Rotary | PW | SD | Display | #
1 | VCC |  | LV | + | GND | GND | GND | GND | 1
2 |  |  |  |  |  |  | MOSI |  | 2
3 |  |  |  |  |  | LV2 |  |  | 3
4 |  |  |  |  |  |  |  |  | 4
5 |  |  |  |  |  |  |  |  | 5
6 |  |  |  |  |  | LV1 |  |  | 6
7 |  |  |  | CLK-1 |  |  |  |  | 7
8 |  |  |  | DT-1 |  |  | MISO |  | 8
9 |  |  |  | SW-1 |  |  | CLK |  | 9
10 |  |  |  | CLK-2 |  |  | CS |  | 10
11 |  |  |  | DT-2 |  |  |  | BL | 11
12 |  |  |  | SW-2 |  |  |  | CLK | 12
13 | (MISO) |  |  |  |  |  |  | RST | 13
14 |  |  |  |  |  |  |  |  | 14
15 | MOSI/DIN |  |  |  |  |  |  | DC | 15
16 |  |  |  |  |  |  |  | CS | 16
17 |  |  |  |  |  |  |  |  | 17
18 |  |  |  |  |  |  |  |  | 18
19 |  | 5V |  |  |  |  |  |  | 19

## Slide 24: SD Modul
ESP
GND
GPIO 19 (VSPI MISO)
GPIO 18 (VSPI SCL)
GPIO 23 (VSPI MOSI)
GPIO 5 (VSPI SS)
5V
MISO (Master In Slave Out)

## Slide 25: Pegel Wandler
BUS | ESP |  | ESP | BUS
GND |  |  | GND | 
VCC (5V) |  |  | 3V3 | 
D+ (SCL) |  |  | GPIO 22 | 
D- (SDA) |  |  | GPIO 21 | 

## Slide 26: Rotary Encoder
LEFT
RIGHT
ESP
GPIO 32
GPIO 33
GPIO 25
3V3
GND
ESP
GPIO 26
GPIO 27
GPIO 14
3V3
GND

## Slide 27
 | SD-Modul | ESP32 Pin | Description
 | 3V3 | 3V3 | Power plus
 | GND | GND | Power minus
 | MISO | GPIO 19 | Master-In-Slave-Out
 | MOSI | GPIO 23 | Master-Out-Slave-In (parallel to DIN of Display)
 | CLK | GPIO 18 | Clock (parallel to CLK of TFT Display)
 | CS | GPIO 5 | Chip Select
USB Port | Pegelwandler | ESP32 | Description
VCC (5V) | HV | V5 | Power plus 5V
GND | GND | GND | Power minus
D- (SDA) | HV1 |  | SDA (high voltage)
D+ (SCL) | HV2 |  | SCL (high voltage)
 | LV | 3V3 | Power plus 3.3V
 | LV1 | GPIO 21 | SDA (low voltage)
 | LV2 | GPIO 22 | SCL (low voltage)
 | Display Pin | ESP32 Pin | Description
 | VCC | 3V3 | Power plus
 | GND | GND | Power minus
 | CS | GPIO 15 | SPI Chip Select
 | RST | GPIO 4 | Display Reset
 | DC | GPIO 2 | Data / Command Selection
 | - | GPIO 12 | MISO (in case of touch pad)
 | DIN (SDI, MOSI) | GPIO 13 | SPI-Datenausgang vom ESP32 (MasterOut-SlaveIn)
 | CLK | GPIO 16 | SPI Hardware-Taktleitung
 | BL | GPIO 17 | Hintergrundbeleuchtung regelbar (oder dauerhaft an)
 | Rotary Encoder | ESP32 Pin | Description
 | LEFT CLK | GPIO 32 | CLK at Rotary Encoder on left side
 | LEFT DT | GPIO 33 | DT at Rotary Encoder on left side
 | LEFT SW | GPIO 25 | SW at Rotary Encoder on left side
 | RIGHT CLK | GPIO 26 | CLK at Rotary Encoder on right side
 | RIGHT DT | GPIO 27 | DT at Rotary Encoder on rght side
 | RIGHT SW | GPIO 14 | SW at Rotary Encoder on right side

## Slide 28: Backlight Pin (BL)
Typsches Setup:
Arduino PWM-Pin → 100–220 Ohm Widerstand → BL-Pin
Dann mit analogWrite(pin, 0-255) die Helligkeit steuern
Beim Arduino funktioniert das so:
analogWrite(pin, 0); // 0 = komplett aus
analogWrite(pin, 128); // 128 = halbe Helligkeit
analogWrite(pin, 255); // 255 = volle Helligkeit
Für deinen BL-Pin am Display reicht aber auch einfach:
digitalWrite(BL_Pin, HIGH); // Backlight an
digitalWrite(BL_Pin, LOW); // Backlight aus
Wenn du nur an/aus brauchst, ist digitalWrite völlig ausreichend – PWM (Pulsweitenmodulation) brauchst du nur, wenn du die Helligkeit stufenlos regeln möchtest.

## Slide 29: Datenleitungen schützen
Spannungsteiler aus Widerständen: Schalte in jede Signalleitung vom Arduino Nano zum Display (MOSI, SCK, CS, D/C, RESET) einen einfachen Spannungsteiler. Ein 1kΩ Widerstand in Reihe und ein 2kΩ Widerstand gegen Masse (GND) senkt das 5V-Signal des Nano absolut sicher auf displayfreundliche ca. 3,3V ab. Das ist bei SPI-Frequenzen bis zu mehreren Megahertz absolut stabil.

## Slide 30: Datenleitungen schützen

## Slide 31: Lingo Bingo

## Slide 32: Lingo Bingo Gadget
Würfelähnliches Spiel
  6 LEDs die die Würfelaugen repräsentieren
  Ausgabe Jingle Sound während würfeln
  Ausgabe gewürfelte Ziffer Sound in unterschiedlichen Sprachen
Taste : es wird normal gewürfelt
Numpad Eingabe : es wird gewürfelt und bei Treffer entsprechend honoriert

## Slide 33
# | LED |  |  | #
1 | CLK |  |  | 1
2 |  |  |  | 2
3 |  |  |  | 3
4 |  |  |  | 4
5 |  |  |  | 5
6 |  |  |  | 6
7 |  |  |  | 7
8 |  | SDA |  | 8
9 |  | SLC |  | 9
10 |  |  |  | 10
11 |  |  | LED-1 | 11
12 |  |  |  | 12
13 |  |  |  | 13
14 | GND | GND |  | 14
15 |  | 5V |  | 15

## Slide 34: Lingo Bingo Controls
Panel
inkl. nut : 115 x 133
innen : 100 x 120
LED Kreis
von oben: 50
Radius: 30
Charging USB (links)
- Links :
0,77 cm
0,77 cm
6
1
3
4
2
5

## Slide 35: Lingo Bingo Frame
Frame
außen : 136 x 156
innen : 100 x 120
Rand : 18
Fizz Bizz
Lingo Bingo

## Slide 36
Frame
Breite : 86

## Slide 37: Storybook

## Slide 38: Storybook Gadget
Geschichtenerzähler
  diverse interaktive Geschichten
  Auswahl der Geschichte
  Jede Geschichte eingeteilt in Abschnitte
  Optional : kein linearer Durchlauf, sondern gesteuert durch das Kind
Start Button (grüne LED)
  wenn der start button (unterhalb der grünen LED) gedrückt wird, werden die konfigurierten Stories hintereinander angezeigt
  während dieses "Selection" Modus wird eine grüne LED angezeigt
  es wird jeweils ein sound und ein bitmap geöffnet – quasi als teaser
  es werden alle Stories nur einmal gezeigt, dann wird der Selektionsmodus beendet
Select Button (blaue LED)
  während des Selektionsmodus kann die gerade angezeigte Story ausgewählt werden.
  dies erfolgt durch drücken des Select Buttons (unterhalb der blauen LED)
  damit wird der Selektionsmodus beendet (grüne LED erlischt) und der Reading Modus beginnt (blaue LED an)

## Slide 39
# | SD | PW |  |  |  | PW | SD | #
1 |  | LV |  |  |  | GND | GND | 1
2 |  |  |  |  |  |  | MOSI | 2
3 |  |  |  |  |  | LV2 |  | 3
4 |  |  |  |  |  |  |  | 4
5 |  |  |  |  |  |  |  | 5
6 |  |  |  |  |  | LV1 |  | 6
7 |  |  | START_BUTTON |  |  |  |  | 7
8 |  |  | SELECT_BUTTON |  |  |  | MISO | 8
9 |  |  | SELECTING_LED |  |  |  | CLK | 9
10 |  |  | READING_LED |  |  |  | CS | 10
11 |  |  |  |  |  |  |  | 11
12 |  |  |  |  |  |  |  | 12
13 |  |  |  |  |  |  |  | 13
14 |  |  |  |  |  |  |  | 14
15 |  |  |  |  |  |  |  | 15
16 |  |  |  |  |  |  |  | 16
17 |  |  |  |  |  |  |  | 17
18 |  |  |  |  |  |  |  | 18
19 | 5V |  |  |  |  |  |  | 19

## Slide 40: SD Modul
ESP
GND (rechts 1)
GPIO 19 (VSPI MISO, rechts 8)
GPIO 18 (VSPI SCL, rechts 9)
GPIO 23 (VSPI MOSI, rechts 2)
GPIO 5 (VSPI SS, rechts 10)
5V (links 19)
MISO (Master In Slave Out)

## Slide 41: Pegel Wandler
BUS | ESP |  | ESP | BUS
GND |  |  | GND (rechts 1) | 
VCC (5V) |  |  | 3V3 (links 1) | 
D+ (SCL) |  |  | GPIO 22 (rechts 3) | 
D- (SDA) |  |  | GPIO 21 (rechts 6) | 

## Slide 42
 | SD-Modul | ESP32 Pin | Description | 
 | 3V3 | 3V3 | Power plus | 
 | GND | GND | Power minus | 
 | MISO | GPIO 19 | Master-In-Slave-Out | 
 | MOSI | GPIO 23 | Master-Out-Slave-In (parallel to DIN of Display) | 
 | CLK | GPIO 18 | Clock (parallel to CLK of TFT Display) | 
 | CS | GPIO 5 | Chip Select | 
USB Port | Pegelwandler | ESP32 | Description | 
VCC (5V) | HV | V5 | Power plus 5V | 
GND | GND | GND | Power minus | 
D- (SDA) | HV1 |  | SDA (high voltage) | 
D+ (SCL) | HV2 |  | SCL (high voltage) | 
 | LV | 3V3 | Power plus 3.3V | 
 | LV1 | GPIO 21 | SDA (low voltage) | 
 | LV2 | GPIO 22 | SCL (low voltage) | 

## Slide 43: Settings

## Slide 44: Portsettings
Module | Module ID | COM Port
Display Module | 0x11 | COM 13
Sound Module | 0x10 | COM 12
Dice Gadget | master | COM 10
Storybook Gadget | master | COM 9
Numpad Board | 0x20 | -
Computer\HKEY_LOCAL_MACHINE\SYSTEM\CurrentControlSet\Control\usbflags IgnoreHWSerNum : DWORD = 1

## Slide 45: extras

## Slide 46
# | SD |  | SD | #
1 | CLK |  | MISO | 1
2 |  |  | MOSI | 2
3 |  |  | CS | 3
4 |  |  |  | 4
5 |  |  |  | 5
6 |  |  |  | 6
7 |  |  |  | 7
8 |  | SDA |  | 8
9 |  | SLC |  | 9
10 |  |  |  | 10
11 |  |  |  | 11
12 |  |  |  | 12
13 |  |  |  | 13
14 | GND | GND |  | 14
15 |  | 5V |  | 15

## Slide 47: SD Modul
MISO

## Slide 48
Gadget A I2C Port (USB)
USB Pin Mapping
G : GND
D- : SDA (Ardino A4)
D+ : SCL (Ardino A5)
V : 5V
more Gadgets … I2C Port (USB)
Arduino Nano
Gadget Board A
Service Port (USB)
I2C Port (USB)
A5
A4
D+
D-
GND
V
5V
GND
USB Power Mapping
only V5 and GND are provided
Charging (USB)
Power Out
Port (USB)
Power Supply Board
Li Battery Pack
TP4056
MT3608
Arduino Nano
Power / Service Port (USB)
Master Board
DFPlayer Mini
common components
A5
A4
5V
GND
Computer
Arduino IDE
software upload
debugging
D+
D-
GND
V

## Slide 49
Gadget A I2C Port (USB)
USB Pin Mapping
G : GND
D- : SDA (Ardino A4)
D+ : SCL (Ardino A5)
V : 5V
more Gadgets … I2C Port (USB)
Arduino Nano
Gadget Board A
Service Port (USB)
I2C Port (USB)
A5
A4
D+
D-
GND
V
GND
USB Power Mapping
only V5 and GND are provided
Charging (USB)
Power Out
Port (USB)
Power Supply Board
Li Battery Pack
TP4056
MT3608
Arduino Nano
Power / Service Port (USB)
Master Board
DFPlayer Mini
common components
A5
A4
5V
GND
Computer
Arduino IDE
software upload
debugging
D+
D-
GND
V
switch V

## Slide 50
TF Card, FAT32, Folder "mp3"
Files "0001.mp3" … "0004.mp3"
Button Field
T1
T4
GND
…
brown-black-red 1 k Ohm
DFPlayer Mini
VCC Pin 1
GND Pin 7
RX Pin 2
TX Pin 3
SPK_1 Pin 6
SPK_2 Pin 8
Speaker 8 Ohm
Battery Box
4,5 V
GND
VCC
+
-
GND
Light Field
L1
L4
…
+
+
-
-
red-red-brown 220 k Ohm
red-red-brown 220 k Ohm
…
100 µF
+
-
D10 / TX
D11 / RX
D7
D4
Arduino Nano
VCC
GND
…
D11
D8
…
A0
Poti
VCC Pin 1
GND Pin 3
Pin 2
Master Switch

## Slide 51
https://wokwi.com/projects/474422651455561729
https://wolles-elektronikkiste.de/dfplayer-mini-ansteuerung-mit-dem-arduino

## Slide 52: PCF8574 Masterselect
Activity Bus Connect
ESP | Rotary Encoder | Relais
 | CLK | 
 | DT | 
 | SW | 
 |  | IN1
 |  | IN2
 |  | IN3
 |  | IN4
25 |  | 
2 x Relay Module für VCC und SCL

## Slide 53
https://sonniss.com/category/sound-libraries/bundles/
https://sfxr.me/
https://www.myinstants.com/en/search/?name=pacman